## Slide 1: STFC in PaNOSC Catalin Condurache – STFC UKRI Photon – Neutron Working Meeting EOSC-hub Week 2019, Prague

## Slide 2: What is STFC doing in PaNOSC?
Providing the tools for moving large data sets around.
The provisioning and support of data transfer will be organized in two phases:
  PY1: Alpha testing including requirements analysis, piloting, porting of existing applications to FTS3, FTS3 operations (effort: 4 PM)
  PY2-3-4: Beta testing including FTS3 operations in pre-production at higher data transfer rates, support to users and service providers (effort: 1 PM/year)
Storing ~1PB of data per year for the 4 years.
  Agreement in principle from IRIS project to fund hardware.
The data infrastructure will be operated in two phases:
  PY1: setting up of the infrastructure and service enabling by PaNOSC applications (Effort: 8 PM)
  PY2-3-4: operations and support (effort: 3 PM/year)

## Slide 3: ECHO – The Ceph Object Store for PaNOSC
Provided by RAL Tier-1 facility, hosted by Scientific Computing Department, part of STFC
Ceph
  Highly-reliable, fast, object store
  Industry-standard protocols
  Convenient interface
ECHO is the main SCD’s main Ceph cluster
  It provides disk storage for the WLCG experiments
  ~250 storage nodes providing 44PB RAW storage
  Data is secured using Erasure Coding (8+3)
    Files are stored across 11 different storage nodes. Can survive the loss of any 3 entire storage nodes

## Slide 4: ECHO – The Ceph Object Store for PaNOSC
ECHO uses the Ceph Gateway to provide access to the object store through the Amazon Web Service S3 or OpenStack Protocols
Using these HTTP-based protocols allows for the possibility of adding extra storage resources from public cloud providers, such as AWS

## Slide 5: DynaFed – an Access and Presentation Layer for ECHO
CERN has developed DynaFed as a means of federating access to storage clusters. It is particularly useful for object storage clusters such as ECHO.
DynaFed can provide:
  An Access Layer (X509 or allowing users to authenticate with their home institution credentials)
  Secure access to objects, whilst not exposing system access keys to users
  A web interface allowing a hierarchical view of the flat object store (simulating a directory layout)

## Slide 6: File Transfer Service - FTS
Data movement service
Open source software to transfer data reliably and at large scale between storage systems
Developed by CERN
Distributes the majority of Large Hadron Collider data across the Worldwide LHC Computing Grid (WLCG) infrastructure
STFC runs a FTS instance for WLCG and beyond
FTS OLA between STFC and EGI.eu

## Slide 7: FTS & DynaFed
DynaFed[1] provides an authentication and authorization layer in front of Cloud storage.
  Also handles protocol translation if necessary.
Currently X.509 auth methods, but also support for OpenID-Connect (XDC project)
DynaFed
Site A Storage
Echo S3
Gateway
FTS
Ceph backend
ssh
S3
GridFTP, XRootD,
S3
[1] http://lcgdm.web.cern.ch/dynafed-dynamic-federation-project

## Slide 8: Non-X509 Auth for FTS & DynaFed
FTS developers will follow the outcome of the WLCG Authz WG which will drive the future WLCG auth/authz methods
Probably token based auth via OpenID-Connect, with usage of Token translation for X509 compatibility
[1] http://lcgdm.web.cern.ch/dynafed-dynamic-federation-project